## Slide 1: CS 423 – Operating Systems Design Lecture 22 – Power Management
Klara Nahrstedt and Raoul Rivas
Spring 2013

## Slide 2: Overview
Administrative announcements
  MP3 still going
Summary
  ACPI
  CPU Management
    DVS, Sleep States
  Wireless Management
  Hard-Drive Management
  Software Approaches

## Slide 3: Importance of Power Management
Mobile Devices are ubiquitous
  Laptops, iPads, Smartphones
  Battery is the limiting factor of these devices
Power Management is driven by
  More functionality
  More processing
  Longer battery lifetime
  Smaller factor devices (weight and size)
Battery capacity is improving at much slower rate

## Slide 4: Mobile Computing Improvement

## Slide 5: Approaches to Reduce Energy Consumption
Turn off parts of the computer when are not in use (mostly IO devices such as display)
  Reduced responsiveness/performance
  Which hardware/software component takes most energy?
Software Approaches
  Reduced responsiveness/performance

## Slide 6: Idle Power Consumption Breakdown

## Slide 7: ACPI
Advanced Control Power Interface
  Open Standard for device configuration and power management
  By Intel, Microsoft, Toshiba – 1996
  Interface between OS and Hardware
Defines Power States
  Global System (G and S States)
  Device (D-State), Processor (C-State)
Defines Performance States (P-States)
  Device, Processor

## Slide 8: ACPI States
Suspend to RAM
Suspend to Disk
Device Power States
Global States
CPU Performance
States
CPU Power
States

## Slide 9: CPU Power States
Used when CPU is idle for some time
Power State Approaches
  Stop Core and Bus Clock
  Clear Caches
  Reduce Processor’s Voltage
Deeper States incur higher transition latency
  Performance reduction
  Effective only when sleeping for long time
Loss of Functionality
  Unable to handle interrupts
  Cold Cache after wake up

## Slide 10: CPU Performance States
Used when the CPU is not fully idle
Implemented using Dynamic Voltage Scaling
  Reduce CPU’s Voltage and Frequency
    AMD Cool’n Quiet, Intel SpeedStep
  Manufacturers try to minimize transition latency
Performance is degraded
  Assumption is that CPU Bandwidth is larger than currently required
  OS implements Adaptive Schemes
    Adjust based on short term statistical CPU utilization

## Slide 11: CPU Power Consumption
Dynamic Power: Power consumed by charging and discharging the capacitance at each gate
  A: % of gates switching each clock
  C: Total capacitance of all gates (Store Energy)
  V: Voltage
  f: Frequency
Dynamic Power
Short Circuit Power
Leakage Power

## Slide 12: CPU Power Consumption
Short Circuit Power: Flow of energy between the supply voltage and ground while the CMOS gates switch
  A: % of gates switching each clock
  Ishort: Current
  t: Time
  V: Voltage
  f: Frequency
Dynamic Power
Short Circuit Power
Leakage Power

## Slide 13: CPU Power Consumption
Leakage Power: Energy lost by powering the die
  Ileak: Current
  V: Voltage
Dynamic Power
Short Circuit Power
Leakage Power
Dynamic Power is the dominating term in this equation
Due to Hardware constraints if we reduce Voltage we must also reduce operating Frequency

## Slide 14: Dynamic Voltage Scaling Example
Power (W) vs. Core Voltage (V) for Intel Pentium-M 1.6 Ghz. Source: Intel Corp.

## Slide 15: Hard-Drive Power Management
Spin-down platters
  Higher Latency (Spin Up Time)
  Increased Wake-Up Energy Consumption
    Friction, Inertia
Slow-down platter rotation
  Green Hard Drives
  Lower Transfer Rate
  Higher Seek Time

## Slide 16: Wireless Power Management
Radio Listening is expensive
Can we turn off the antenna to save power?
  Notify the Access Point
  Turn off client antenna
  AP buffers packets and periodically notify clients on who has packets
  Client Polls the Access Point for stored Packets

## Slide 17: Software Aproaches
Power Aware-Scheduling
  Linux Power-aware Scheduler
    Do not distribute the load across cores.
    Aggregate all tasks in one core so other cores can sleep
  GraceOS
    Power-aware Real-time Scheduler
    University of Illinois Research Project
Imprecise Computing
  Reduce the precision of your computation so CPU sleeps more

## Slide 18: Software Aproaches
Group Timers
  Aggregate multiple timers into one
    One interrupt for many timers
    Longer sleep time
Tickless Kernel
  Do not use periodic timer to measure time
  Update time when other event/interrupt occurs
Group Timer
Standard Timer

## Slide 19: Grace OS
Power aware scheduler for Multimedia
  Minimize Power Consumption
  Trade-off between Quality and Power
Realtime Scheduler
  Earliest Deadline First policy
Dynamic Voltage Scaling
  Reduce CPU Speed as much as possible without missing any deadlines
Online Application Profiler
  Adapt the CPU Reservation to the actual utilization of the application

## Slide 20: Grace OS Architecture

## Slide 21: Summary
Power management is important
  Battery, Cooling Costs, Environment
Power savings come at cost
  Reduced Performance
  Higher Latency
Basic Principles
  Amdhal’s Law
  Power off idle systems
  Slow down underutilized systems